## Slide 1: Defending Against Man-in-the-Middle Attacks on AODV Routing
Andrew Fallgren
Aaron Pope
George Rush

## Slide 2: What is AODV Routing?
Ad-hoc On Demand Distance Vector Routing (AODV)
This is the routing protocol used in ZigBee, a popular standard for wireless mesh networks.
A mesh network is a topology in which each node relays data for the network.

## Slide 3: How does AODV work?
Original sender broadcasts Route Request (RREQ).
A
B

## Slide 4: How does AODV work?
Intermediate nodes propagate RREQ.
A
B

## Slide 5: How does AODV work?
Destination node sends Request Reply (RREP) back to sender for each RREQ.
A
B

## Slide 6: How does AODV work?
Sender uses lowest hop-count route to communicate with destination.
A
B

## Slide 7: Attack Model (Initial Conditions)
Of n deployed nodes, one or more are captured by an adversary.

## Slide 8: Attack Model (Exploitation)
A captured node agrees to forward traffic on a route from Node A to Node B.
A
B

## Slide 9: Attack Model (Exploitation)
The captured node drops all packets rather than forwarding them.
A
B

## Slide 10: Attack Model (Results)
Data loss
  Packets never reach their destination.
Energy loss
  Nodes waste energy on radio communication.

## Slide 11: Defensive Goals
Primary Objective
  Ensure that packets reach their destination if it is possible to do so.
Secondary Objective
  Minimize message complexity in order to reduce network transmissions.

## Slide 12: Sources
Perkins, Charles E., and Elizabeth M. Royer. "Ad-hoc on-demand distance vector routing." Mobile Computing Systems and Applications, 1999. Proceedings. WMCSA'99. Second IEEE Workshop on. IEEE, 1999.
http://en.wikipedia.org/wiki/ZigBee
http://en.wikipedia.org/wiki/Mesh_networking
Images from openclipart.org