## Slide 1: Defending Against Man-in-the-Middle Attacks on AODV Routing
Andrew Fallgren
Aaron Pope
George Rush

## Slide 2: What is AODV Routing?
Ad-hoc On Demand Distance Vector Routing (AODV)
This is the routing protocol used in ZigBee, a popular standard for wireless mesh networks.
A mesh network is a topology in which each node relays data for the network.

## Slide 3: How does AODV work?
Original sender broadcasts Route Request (RREQ).
A
B

## Slide 4: How does AODV work?
Intermediate nodes propagate RREQ.
A
B

## Slide 5: How does AODV work?
Destination node sends Request Reply (RREP) back to sender for each RREQ.
A
B

## Slide 6: How does AODV work?
Sender uses lowest hop-count route to communicate with destination.
A
B

## Slide 7: Wormhole Attack (Initial Conditions)
Two or more nodes are deployed by an adversary. Capture is unnecessary.

## Slide 8: Wormhole Attack (Getting Selected)
Each pair of deployed enemy nodes creates a tunnel using long-range directional antennas (to offer the shortest path for many routes).
A
B

## Slide 9: Black Hole Attack (Exploitation)
The enemy nodes drop all packets rather than forwarding them.
A
B

## Slide 10: Attack Model (Results)
Data loss
  Packets never reach their destination.
Energy loss
  Nodes waste energy on radio communication.

## Slide 11: Defensive Goals
Primary Objective
  Detect whether or not packets reach their destination. Pick a new route if too many packets are being dropped.
Secondary Objective
  Minimize message complexity in order to reduce network transmissions.

## Slide 12: Related Work

## Slide 13: Related Work

## Slide 14: Related Work

## Slide 15: Our Approach
Routes in AODV must be periodically refreshed.
Source knows the number of data packets sent, and Destination knows the number received.
  Exchange # of packets sent/received when refreshing routes.
AODV floods the network when establishing routes.
  A polling of the neighbors can be used to detect deception by enemy nodes. Once detected, pick a new route.

## Slide 16: Advantages
Minimal changes to AODV.
  Two new integer data fields.
Zero encryption required.
  Not computationally intensive.
Does not increase message complexity.
  Better battery life.
Int
Int

## Slide 17: Evaluation
We need to compare our solution to other techniques for preventing or countering black hole attacks.
Suggested approach: Build a network simulation and test various attack scenarios.

## Slide 18: Network Simulation
Network is represented as a graph.
  Edges connect nodes in communication range.
Random nodes are chosen to form routes using AODV.
  Dummy messages are sent one or both ways to simulate data transactions.
Attackers attempt to execute black hole attacks per various scenarios.
Simulation ends after a fixed period of time.

## Slide 19: Attack Scenarios
No black holes occur.
  This would help test how proposed solutions affect normal network operation.
A single black hole is formed.
  This would show how proposed solutions work under ideal conditions.
Multiple black holes are formed.
  This would test what happens when the enemy has greater capabilities and can further disrupt the network.

## Slide 20: Evaluation Metric
Two main concerns:
  Number of lost messages (L)
  Message complexity of proposed solution (M)
Minimizing L increases availability.
Minimizing M decreases power usage.
The end user can prioritize either one if we view this as a multi-objective problem.
  This means the user can decide the relative weight of both metrics.

## Slide 21: Sources
Images from openclipart.org